Baby Lock Destiny

(Model BLDY)

Software Update Version 1.13

###### December, 2014

Introduction

###### If the software version of your Destiny (Model BLDY) is earlier than version 1.13, an update program is now available for download to improve its performance.

Version 1.13 update will provide the following changes:

- Added 30 additional tutorial videos.

- Improved functionality of the following features:

    - IQ Designer

    - Camera

To confirm the software version of your BLDY

- Press the power switch to "|" to turn on your machine.

- If the opening movie is played, touch anywhere on the LCD screen.

- Press  (Machine setting mode key) to display the machine's settings screen.

- The machine's settings screen appears.

- Switch the settings screens by using  (Previous page key) or  (Next page key) to display the machine's program version.

- If "Version" shown in the screen is already "1.13" or later, it is not necessary to update your machine with the software on this page.

How to download the update program

- Create a temporary folder (ex. C:\Temp) on your computer to save the update program file to be downloaded.

- Click the “Download FILE” below.

- Select the previously created temporary folder (ex. C:\Temp) where the downloaded file should be stored.

- Download the file.

[1/2] 	Download FILE  (xv_movie_file_taco_N.upf, size: 567 MB) 

[2/2] 	Download FILE  (XV_V113_taco_Cmb_P.upf, size: 85.1 MB)

How to update your machine’s software

There are two update files for updating the machine to version 1.13.
Each update file should be loaded into the machine as follows.

- Insert the USB Flash drive into the USB port on the computer.

- Copy the first update file (xv_movie_file_taco_N.upf) to the USB Flash drive.
          NOTE:
             The USB Flash drive should be a reformatted 4GB or higher flash drive
            that contains the first update file only.

- Safely remove the USB Flash drive from the USB port on the computer.

- While pressing the "Automatic Threading" button, turn the main power to ON.
The following screen will appear on the LCD.

- Press the USB media key.

- Insert the USB Flash drive into the primary (top) USB port on the machine.

- Press the LOAD key.

- When the message "Upgrade complete" appears, the first update file has been loaded.

- Turn the machine off.

- Remove USB Flash drive from the USB port on the machine.

- Insert the USB Flash drive into the USB port on the computer.

- Delete the first update file in the USB Flash drive by reformatting, and then,
      copy the second update file (XV_V113_taco_Cmb_P.upf) to the USB Flash drive
          NOTE:
             The USB Flash drive should contain the second update file only.

- Safely remove the USB Flash drive from the USB port on the computer.

- While pressing the "Automatic Threading" button, turn the main power to ON.
The following screen will appear on LCD.

- Press the USB media key.

- Insert the USB Flash drive into the primary (top) USB port on the machine.

- Press the LOAD key.

- When the message "Upgrade complete" appears, the update is completed.

- Turn the machine off.

- Remove the USB Flash drive from the USB port on the machine.

- Turn the machine on.

- Your machine's software has been updated to version 1.13.

When the update completed successfully, "Version" on the settings screen shows "1.13".

If "Version" on the settings screen shows “1.13#”, the first update file was not installed.
	Install the first update file (xv_movie_file_taco_N.upf) into the machine.

* * * NOTE * * * Do not turn off your machine while the machine is saving the update software to itself. If the machine's power is turned off while saving the update software, it may result in damage to the machine. When using USB Flash drive (USB Flash memory) to update the machine’s software, check that no data except for the update file is saved on the USB Flash drive (USB Flash memory) being used before beginning update. Connecting a computer to the machine using a USB cable is not available to update the machine on this update.

Baby Lock Destiny (Model BLDY) Update History

- Version 1.12 update provided the following changes.

- Fixed some issues which may have occurred when the machine starts up.

- Fixed some issues with the machine regarding the following features.

    - Pivot function

    - Camera function

    - IQ Designer

- Version 1.11 update provided the following changes.

- Fixed some issues which may have occurred when the machine starts up.

- Fixed some issues with the machine regarding the following features.

    - Scanning fabric to be used as a background with the Super Large Embroidery Frame (9.5” x 14”)

    - Connecting the rotated patterns using the camera function

    - IQ Designer

    - Reading the pattern data from USB DVD/CD drive

- Version 1.10 update provided the following changes.

- The USB mouse (optional accessory) is available.

- The Embroidery card reader (optional accessory) is available.

- Connecting a computer to the machine using a USB cable will be supported to update the machine's software after updating to version 1.10. (Windows OS only)